Parallel Image/Video Editor
Adam Feinstein and H. Parker Shelton, 520.443, Johns Hopkins University

---
Project Overview
GPU-Parallelized Image and Video Editor
Multiple Encoding Algorithms

---
Nvidia’s CUDA
- Compute-Unified Device Architecture
- GPU (grid) divided into Blocks, Threads
- Each Thread invokes the same kernel, preforms its own calculations

---
Nvidia’s CUDA
- Threads can share memory, Blocks cannot
- Memory must be copied from the host to the GPU and back again

---
Qt
Cross-Platform C++ GUI Framework
Multi-threading, Multimedia, WebKit, SQL

---
GUI Demonstration

---
Image Editing
Grayscale
Brightness
Contrast
Saturation
Crop
Rotate
Scale
Blur
Edge Detect

---
Grayscale
// Replace each RGB with the luminance value
for(int y = 0; y < img->height(); y++) {
     for(int x = 0; x < img->width(); x++) {
        QRgb p = img->pixel(x, y);
        r = g = b = (qRed(p) * 0.3) + (qGreen(p) * 0.59) + (qBlue(p) * 0.11);
        img->setPixel(x, y, qRgb(r, g, b));
     }
}
return img;

---
GPU: Grayscale
extern "C" void CUgreyscale(unsigned char* output, unsigned char* input, int row, int col);
void CUgreyscale(unsigned char* output, unsigned char* input, int row, int col)
{
dim3 dimGrid(row/16+1, col/16+1);
dim3 dimThreadBlock(16,16);
greyscale<<<dimGrid, dimThreadBlock>>>(input, output, row, col);
}
__global__ void greyscale(unsigned char* input, unsigned char* output, int row, int col)
{
int xIndex = blockDim.x * blockIdx.x + threadIdx.x;
int yIndex = blockDim.y * blockIdx.y + threadIdx.y;
int index = (4*xIndex + yIndex * row*4);
if(index < row*col*4){
int lum = 0.11*input[index] + 0.59*input[index+1] + 0.3*input[index+2];
output[index]=lum;
output[index+1]=lum;
output[index+2]=lum;
output[index+3]=0;
}
}

---
Brightness
// Scale each RGB value by the brightening factor
for(int y = 0; y < img->height(); y++) {
     for(int x = 0; x < img->width(); x++) {
        QRgb p = img->pixel(x, y);
        int r = qRed(p) * factor;
        int g = qGreen(p) * factor;
        int b = qBlue(p) * factor;
        // Clamp color values
        img->setPixel(x, y, qRgb(r, g, b));
     }
}
return img;

---
Contrast
// Scale each RGB value away from the average luminosity
for(int y = 0; y < img->height(); y++) {
     for(int x = 0; x < img->width(); x++) {
        QRgb p = img->pixel(x, y);
        int r = (1-factor)*average_lum + factor*(qRed(p));
        int g = (1-factor)*average_lum + factor*(qGreen(p));
        int b = (1-factor)*average_lum + factor*(qBlue(p));
        // Clamp color values
        img->setPixel(x, y, qRgb(r, g, b));
     }
}
return img;

---
Saturation
// Scale each RGB value away from its luminosity
for(int y = 0; y < img->height(); y++) {
     for(int x = 0; x < img->width(); x++) {
        QRgb p = img->pixel(x, y);
        float lum = (qRed(p) * 0.3) + (qGreen(p) * 0.59) + (qBlue(p) * 0.11);
        int r = (1-factor)*lum + factor*(qRed(p));
        int g = (1-factor)*lum + factor*(qGreen(p));
        int b = (1-factor)*lum + factor*(qBlue(p));
        // Clamp color values
        img->setPixel(x, y, qRgb(r, g, b));
     }
}
return img;

---
Crop
// Validate input dimensions and coordinates
// Copy pixels within the coordinates
for(int x = leftX; x < rightX; x++) {
     for(int y = leftY; y < rightY; y++)
        img->setPixel(x-leftX, y-leftY, img->pixel(x,y));
}
return img;

---
Rotate
// Determine new dimensions
// Rotate the image
for(int x = 0; x < newWidth; x++) {
     for(int y = 0; y < newHeight; y++) {
        float u = cos(-1*a)*(x-newxcenter) - sin(-1*a)*(y-newycenter)+width/2;
        float v = sin(-1*a)*(x-newxcenter) + cos(-1*a)*(y-newycenter)+height/2;
        // Perform Gaussian sampling to determine pixel color
        newImg->setPixel(x, y, Utility::GaussianSample(img, u, v, 0.6, 4));
     }
}
return newImg;

---
Scale
// Determine new dimensions
// Scale the image
for(int x = 0; x < newWidth; x++) {
     for(int y = 0; y < newHeight; y++) {
        float u = 1/factor*x;
        float v = 1/factor*y;
        // Perform sampling to determine pixel color
        newImg->setPixel(x, y, Utility::GaussianSample(img, u, v, 0.6, 2*factor));
     }
}
return newImg;

---
Blur
// Convolution mask
float mask[3][3] = { {1/16.0, 2/16.0, 1/16.0}, {2/16.0, 4/16.0, 2/16.0}, {1/16.0, 2/16.0, 1/16.0} };
for(int y = 0; y < height; y++) {
     for(int x = 0; x < width; x++) {
        int r = 0, g = 0, b = 0;
        for(int i = 0; i <= 2; i++) {
        for(int j = 0; j <= 2; j++) {
        QRgb pixel = img->pixel(x+(j-1), y+(i-1));
        r += mask[i][j]*qRed(pixel);
        g += mask[i][j]*qGreen(pixel);
        b += mask[i][j]*qBlue(pixel);
        }
        }
        // Clamp color values
     }
}
newImg->setPixel(x, y, qRgb(r, g, b));
return newImg;

---
Edge Detect
// Convolution mask
float mask[3][3] = { {-1.0, -1.0, -1.0}, {-1.0, 8.0, -1.0}, {-1.0, -1.0, -1.0} };
for(int y = 0; y < height; y++) {
     for(int x = 0; x < width; x++) {
        int r = 0, g = 0, b = 0;
        for(int i = 0; i <= 2; i++) {
        for(int j = 0; j <= 2; j++) {
        QRgb pixel = img->pixel(x+(j-1), y+(i-1));
        r += mask[i][j]*qRed(pixel);
        g += mask[i][j]*qGreen(pixel);
        b += mask[i][j]*qBlue(pixel);
        }
        }
        // Clamp color values
     }
}
newImg->setPixel(x, y, qRgb(r, g, b));
return newImg;

---
GPU: Edge Detect
extern "C" void CUedgeDetect(unsigned char* input, unsigned char* output, int row, int col);
void CUedgeDetect(unsigned char* output, unsigned char* input, int row, int col)
{
dim3 dimGrid(row/4+1, col/4+1);
dim3 dimThreadBlock(16,16);
float coeff[9]= {-1, -1, -1, \
  -1, 8, -1, \
  -1, -1, -1};
float* CUcoeff;
cutilSafeCall(cudaMalloc((void**)&CUcoeff, sizeof(float)*9));
cutilSafeCall(cudaMemcpy(CUcoeff, coeff, sizeof(float)*9, cudaMemcpyHostToDevice));
conv3x3<<<dimGrid, dimThreadBlock>>>(input, output, row, col, CUcoeff);
cutilSafeCall(cudaFree(CUcoeff));
}

---
GPU: Edge Detect
__global__ void conv3x3(unsigned char* input, unsigned char* output, int row, int col, float* kernel)
{
int xIndex = blockDim.x * blockIdx.x + threadIdx.x;
int yIndex = blockDim.y * blockIdx.y + threadIdx.y;
int index = (xIndex + yIndex * row*4);
if(index < row*col*4){
int i, j;
float convSum=0;
for(i=-1; i < 2; i++){
for(j=-1; j < 2; j++){
if(-1 < (index+4*j)+(4*col*i) && (index+4*j)+(4*col*i) < row*col*4){
convSum += kernel[3*(i+1) + (j+1)]*input[(index+4*j)+(4*col*i)];
}
}
}
output[index] = CLAMP(convSum);
}
}

---
CPU vs GPU Speed Comparison
Time, Pixel Operation (greyscale)
world.jpg
X and Y Dimension (pixels)
Time (ms)

---
CPU vs GPU Speed Comparison
Time, 3x3 Convolution (edge detection)
world.jpg
X and Y Dimension (pixels)
Time (ms)

---
Decoding
QImage-provided support for .bmp, .gif, .jpg, .png, .pgm, and .tif decoding
Decoding implemented for custom .ppc codec
Image stored in 32-bit RGBA format internally

---
Encoding
QImage-provided support for .bmp, .jpg, .png, .tif encoding with quality setting option
Encoding implemented for custom .ppc codec
Huffman Compression
Arithmetic Compression
Run Length Compression

---
Encoding
Sully.bmp: 329 Kb
None: 436 Kb
Run Length: 318 Kb
Huffman: 277 Kb
Arithmetic: 874 Kb
Huffman over Run Length: 260 Kb
Arithmetic over Run Length: 636 Kb
Arithmetic over Huffman: 554 Kb
Arithmetic over Huffman over Run Length: 528 Kb

---
.ppc Codec
void Encoder::write_ppc(QImage* img, QString filename, bool huffman, bool arithmetic, bool runlength) {
     int mode = 4*runlength + 2*huffman + arithmetic;
     unsigned long numBytes = img->byteCount();
     unsigned char* byte_stream = img->bits();
     double* arithmetic_stream = NULL;
     if(runlength) byte_stream = runlength_encode(byte_stream, &numBytes);
     if(huffman) byte_stream = huffman_encode(byte_stream, &numBytes);
     if(arithmetic) arithmetic_stream = arithmetic_encode(byte_stream, &numBytes);
     FILE* output;
     if(!(output = fopen(filename.toStdString().c_str(), "w"))) { return; }
     fprintf(output, "%d %d %d %lu", mode, width, height, numBytes);
     if(!arithmetic) fwrite(byte_stream, sizeof(unsigned char), numBytes, output);
     else fwrite(arithmetic_stream, sizeof(double), numBytes, output);
     fclose(output);
}

---
Compression
Discrete 9/7 Wavelet Transform, lifting implementation
- Used Grigory Pau's implementation, uses exact coefficients given by Taubman and Marcellin in JPEG2000 paper
  (http://www.embl.de/~gpau/misc/dwt97.c)
- CPU: lightly modified, GPU: heavily modified
- No color transform, still have to sort out colors
- One level transform
- Use piecewise continuous function to approximate threshold for zeroing out coefficients give a desired percent of coefficients zeroed out

---
Compression

---
Compression

---
Compression

---
Compression

---
CPU vs GPU Speed Comparison
Time, Compression
world.jpg
X and Y Dimension (Pixels)
Time (ms)

---
CPU vs GPU Speed Comparison
GPU Limitations:
- cudaMemcpy() still runs in linear time, necessary to move data onto and off of a GPU
- Resources used by operating system, failed to allocate space for a 4096x4096 image (64MB * 2)
- Wavelet transform doesn't use __shared__ memory

---
Video Features
What We Have:
Closed-loop DPCM video coder with uniform scalar quantizer (Basically Assignment III)
CPU Editing Features
What We Don't:
Saving and Opening *.pvc
GPU Compression
GPU Editing Features
Motion Estimation

---
Video Compression
Infinite at 512, didn't include data point

---
Questions?